2D Lesson 2: Circles

This will be a but more complex exercise compared to the two previous ones.

In this exercise, all distances are given but remember that while drawing a circle in AutoCAD that by default, the software will ask you to enter the radius of the circle. In this exercise, however, we are given diameters.
Also remember AutoCAD works by plotting shapes on a grid using (x,y) points exactly. This is very different than Vectorworks and will be tricky to change the way we think.
Make sure Dynamic Input (F12) and Ortho (F3) are still OFF
Start by drawing a line from (0,0) to (10,0)
Draw a circle with its centre at (5,3.5) and a radius of 3.5
Draw a second circle with the same centre point (5,3.5) and a radius of 2
Draw lines starting at (0,0) and then going to (0,-2.5), then (2.5, -2.5)
Continue drawing the lines for the bottom of the shape.
This may take several tries as you get used to figuring out the (x,y) points

To draw the two tangent lines:

Click on the Line tool or type Line in the Command window
Click on one end of the line (W or W')
Hold Ctrl key and Right mouse click
Select Snap Overrides
Select Tangent
Move cursor near the point on the circle where the line is to go, you should see a small red square appear on the circle
Right click to set the other end of the line
Press ESC or Space Bar to end the routine
Repeat the above procedure for the other end of the line

Using the technique above, you should be able to draw the complete figure.