2D Lesson 3: Drawing angles

In this figure, we have a line of length 4.6 at an angle of 49 degrees with the another line of length 2.
To achieve this drawing with AutoCAD, you should first draw the line of length 2, which you should know how to do. Afterwards, start a new line at point A, type @4.6<41 and hit the ENTER key on your keyboard. The command is defined as 4.6 being the length and 41 being the angle in degrees.
However, AutoCAD has a button that will make this much easier. Click the Dynamic Input button on the bottom toolbar or F12. This will allow you to draw this shape much easier.
Are you wondering why 41 degrees when it is stated as 49 in the figure? AutoCAD counts angles in trigonometry form. Therefore, to find the right angle you must do the math, for example, 90 – 49 = 41.
In general, a figure is shown below on how AutoCAD counts angles.

Try this exercise. However, the new part in this exercise consists of the place where you need to draw a line knowing its inclination and its distance. This is shown below:
All dimensions are given.
Hint: turn on ORTHO (F3) for the horizontal and vertical lines, turn on Dynamic Input (F12)for the angled line, and leave the bottom triangle to last. Start drawing from the left of the bottom triangle going left.
For the bottom triangle draw a construction line across the bottom, using your snap override draw an other construction line up from the middle of this line 2.5 high, now draw the angled lines to form the triangle, erase your construction lines.