2D Lesson 5: Chamfer

This exercise can be done with everything you learned in the previous exercises.
 We will add the CHAMFER command as on of your skills today.

The CHAMFER command helps us in getting from point A to B in the figure below:
Start by drawing the outline of the shape but ignore the chamfered section (just square it off).

This being said, we will try creating the following figure:

To get this result, you will have to apply a CHAMFER of 3.2 x 3.2 to the indicated corner.
Follow these steps to use the CHAMFER command:

1 – Click on a CHAMFER icon
2 - (TRIM mode) Current chamfer Dist1 = 0.0000, Dist2 = 0.0000
Select first line or [Undo/Polyline/Distance/Angle/Trim/mEthod/Multiple]: d
3 - Specify first chamfer distance <0.0000>: 3.2
4 - Specify second chamfer distance <3.2000>: 3.2
5 - Select first line or [Undo/Polyline/Distance/Angle/Trim/mEthod/Multiple]: Select A
6 - Select second line or shift-select to apply corner: Select B
On step 4, you could decide to hit the ENTER key without typing 3.2, since the default distance has been already set to that distance from our entry in step 2. AutoCAD will remember Dist1 = 3.2 and Dist2 = 3.2 as a default distance for next use in this file. You are free to change it if in the next use of this command you want Dist1 and Dist2 with different dimensions.
Now the two circles:
If you didn't start your drawing with the bottom left corner at (0,0). You can easily move the drawing to the correct spot.
Select the entire shape by clicking and holding the cursor and drag the rectangle to surround your shape.
Select the Move command from the Modify menu. Click on the bottom left corner of your drawing and type in (0,0), press ENTER. Your drawing should jump to (0,0).
You should now be able to accurately place the two remaining circles into the drawing.